## Slide 1: Independent Study Progress Report Fall 2019
By: Ruairidh Barlow
Mentors: Dr. Chen and Dr. Smirnova

## Slide 2: Project Goals
Use data collected from a Sensor Dot to visualize a subject’s heart rate and breathing rate over the same period of time
Understand the working principles behind ECGs and accelerometers
Learn how to process collected data from both ECGs and accelerometers using MATLAB
  Learn how to program in MATLAB

## Slide 3: Electro - cardio – gram (ECG)
Visualizes the movement of a wave of depolarization through the heart
  Depolarization = positive charge
Wave appearance depends on the set of electrodes being used
  Movement of wave from right arm (ra) electrode to left leg (ll) electrode you get a positive (upward) deflection
Notes: Electricity - Heart – visualize
This example uses that Lead 2, electrode on right arm (ra) and electrode on left leg (ll)
(upward) deflection which reflected in the spike on the graph
Explain lead and axis are terms that can be used interchangeably

## Slide 4: ECG working principle
Electrodes measure the charge on the outside of heart cells
  Resting cells are polarized (negative)
  Wave of depolarization passes through cells, they are then depolarized (positive)
Dipole is when a wave is in the middle of passing through cells
  Dipole vector (arrow) points towards the positive charge
  ECG tracing shows this as a positive (upward) deflection
Notes: Positive and negative electrodes
The bigger the dipole the bigger the deflection

## Slide 5: ECG working principle
There is no dipole when wave of depolarization moves completely through the cells
Results in a flat line, no deflection
Notes: Positive and negative electrodes
The bigger the dipole the bigger the deflection

## Slide 6: ECG working principle
Wave of repolarization (negative)
Dipole vector (arrow) points towards the negative charge
ECG tracing shows this as a negative (downward) deflection
Notes: When the wave isn't moving directly towards an electrode
  Break the dipole vector into the horizontal and vertical components
  We care about the one that is moving towards the electrode
  Since the vectors are smaller, they will have a smaller deflection recorded

## Slide 7: ECG working principle
There are a total of 10 electrodes in a standard ECG
Notes: 4 limb electrodes RA, LA, LL, RL (right leg neutral)
6 precordial electrodes on chest (known as chest leads)
  V1 - V6, line the transverse plane (horizonal) of heart
All are set up to detect any positive wave that comes towards them

## Slide 8: ECG working principle
4 limb electrodes: RA, LA, LL, RL (right leg neutral)
Limb leads that detect positive waves (denoted in purple)
  Use one electrode
Notes: an imaginary plane dividing the body into dorsal and ventral parts
  If you were to cut a person in half between their front and back plane
AVR (augmented vector right)
AVL (augmented vector right)
  Both are vectors that are 30 degrees from heart
AVF (left foot)

## Slide 9: ECG working principle
Bipolar limb leads
  Use 2 electrodes
I: Uses RA and LA moves from negative to positive
II: RA to LL negative to positive at 60 degrees
III: LA to LL, 120 degree angel
There are a total of 6 limb leads
Notes: Denoted in purple as well

## Slide 10: ECG working principle
6 precordial electrodes on chest (chest leads)
  V1 - V6, line the transverse plane of the heart
Total of 6 leads
Notes: Transverse (horizonal)
All detect positive waves
They are all positive electrodes

## Slide 11: ECG working principle
10 electrodes in a standard ECG (RA, LA, RL, LL, V1 - V6)
12 leads make up the standard 12 lead ECG
Notes: It is important to understand that there are 10 electrodes in a standard ECG (RA, LA, RL, LL, V1 - V6).
But there is a total of 12 leads being recorded

## Slide 12: QRS Complex
The combination of three of the graphical deflections seen on a typical ECG
  Usually the main spike seen on the ECG line
The QRS complex lasts 0.06 - 0.12 seconds in adults
Notes: Relate this back to the 2 axis ecg

## Slide 13: II Axis ECG Detection
QRS Complex is clearest when traced using the II axis
Clear tracing allows for accurate signal processing
Notes: https://www.cvphysiology.com/uploads/images/ECG%20stnd%20leads.gif
Understand what each axis can represent better
  If you want to understand what is the p and t wave is doing which axis do you want to look at
    P wave
      Should be upright (positive) in leads 1 and II
      Downright in aVR
    QRS complex
      QRS be mostly positive (upright) in leads II and I
    T wave
      T wave is always upright in leads I, II, V3-6
      Always inverted in lead aVR

## Slide 14: II Axis ECG Detection
Notes: https://www.cvphysiology.com/uploads/images/ECG%20stnd%20leads.gif
Understand what each axis can represent better
  If you want to understand what is the p and t wave is doing which axis do you want to look at
    P wave
      Should be upright (positive) in leads 1 and II
      Downright in aVR
    QRS complex
      QRS be mostly positive (upright) in leads II and I
    T wave
      T wave is always upright in leads I, II, V3-6
      Always inverted in lead aVR

## Slide 15: QRS Complex
Notes: Relate this back to the 2 axis ecg

## Slide 16: Byteflies Sensor Dot
Each sensor contains an array of sensors
  II axis ECG
  Triaxial Accelerometer
Can be used in tandem to collect multiple types of data at the same time
Sensors collect physiological waveforms
Notes: https://www.byteflies.com/science
Electrocardiogram Role (ECG):
Respiration (RES):
Photoplethysmography (PPG): optically obtained plethysmogram that can be used to detect blood volume changes in the microvascular bed of tissue. A PPG is often obtained by using a pulse oximeter which illuminates the skin and measures changes in light absorption
Inertial Measurement Unit (IMU)

## Slide 17: Data Collection Protocol
Adapted from Boyle et al., 2009
10 minutes resting on a bed
5 minutes sitting in a chair
5 minute exercise sessions
  70 kg resistance
  140 kg of resistance
  180 kg resistance
Each followed by 5 minutes of rest in a chair
Notes: https://webstockreview.net/pict/get

## Slide 18: ECG Signal Processing in MATLAB
Filtering data
  Removal of unwanted segments and frequencies from the signal
Feature detection, repeating patterns are selected
  A feature is a recurring shape that tells us something physiologically interesting
Beats Per Minute (BPM) Calculations
Notes: (How it is supposed to be done)
Sometimes a feature can occur at an unpredictable time, like when there is a sudden change in motion
Or they can be cyclical, like a heart beat
  Example: ECG signal, a very large number of features can be extracted
  R-peak, denoting ventricular depolarization; the P-wave, denoting atrial depolarization; and the T-wave, denoting ventricular repolarization

## Slide 19: MATLAB Filtering Data: Import Signal
Notes: Artifact from putting the sensor on

## Slide 20: MATLAB Filtering Data: Import Signal
Notes: Artifact from putting the sensor on
A data artifact is a data flaw caused by equipment, techniques or conditions.
Get x coordinate and

## Slide 21: MATLAB Filtering Data: Import Signal
Notes: Artifact from putting the sensor on

## Slide 22: MATLAB Filtering Data: Fourier Transform
Transforming a signal in the time domain into the frequency domain
Identifies the frequency where signal drift lies
Notes: https://www.youtube.com/watch?v=1JnayXHhjlg
Find the x coordinate
Everything past this point is what will get through the filter
This point is where the signal drift lies
Drifts are signal of low freq

## Slide 23: MATLAB Filtering Data: Butterworth Filter Design
Signal processing filter with a frequency response that is flat as possible
Frequency response is used for peak detection

## Slide 24: Peak Detection
findpeaks function in MATLAB
Peak height and distance parameters are set by hand

## Slide 25: BPM Calculations Functions
Overall BPM for entire signal
Sliding window method
  Overlapping
  Non-overlapping
Peak frequency based method

## Slide 26: Overall BPM Calculation
Count total number of R peaks (beats)for entire signal
Divide signal length by the frequency it was captured at to get seconds
Convert seconds to minutes
Divide number of beats by minutes
Notes: Mention this function is used in windowed as well

## Slide 27: Sliding Window BPM Calculation
MATLAB's buffer function broke up signal into windows of X length
  Parameter for overlap length
Count number of R peaks (beats) in each window
Call overall BMP calculation function (from previous slide)
  Use window length instead of signal length
Store the BPM of each window and calculate the average BPM

## Slide 28: Peak Frequency BPM Calculation
Calculate the distance between peaks
Divide distances by the sampling frequency to convert to seconds
Calculate the frequency of that window between peaks
  Frequency = 60 (seconds/minutes) / distance (seconds)
Notes: https://pt.slideshare.net/cetdmgh/introduction-to-ecg-29796681

## Slide 31: Accelerometer Data
Notes: Y red
Z yellow

## Slide 32: Accelerometer Data
Notes: http://www.bem.fi/book/aa/fi/aa01.gif

## Slide 33: Accelerometer Data
Notes: http://www.bem.fi/book/aa/fi/aa01.gif

## Slide 34: Accelerometer Data
Notes: http://www.bem.fi/book/aa/fi/aa01.gif

## Slide 35: Respiration Signal Derivation (Cysarz et al., 2008 )
Segmented process
Interpolate distances between R peaks
  Maintain original signal as best as possible (intrep1)
Standardize signal
  75th percentile of local maxima
Check for valid cycles
  30th percentile of local maxima

## Slide 36
1.
2.
3.

## Slide 39: What’s next
Attempting to automate this entire process
  This will be very difficult since every person’s heart is different
  Weight, age, and fitness will affect their ECG tracing meaning different filters and peak parameters will have to be tested by hand

## Slide 40: Works Cited
• Boyle, J., Bidargaddi, N., Sarela, A., & Karunanithi, M. (2009). Automatic Detection of Respiration Rate From Ambulatory Single-Lead ECG. IEEE Transactions on Information Technology in Biomedicine,13(6), 890-896. doi:10.1109/titb.2009.2031239
• Cysarz, D., Zerm, R., Bettermann, H., Frühwirth, M., Moser, M., & Kröz, M. (2008). Comparison of Respiratory Rates Derived from Heart Rate Variability, ECG Amplitude, and Nasal/Oral Airflow. Annals of Biomedical Engineering, 36(12), 2085–2094. doi: 10.1007/s10439-008-9580-2
• Documentation. (n.d.). Retrieved from https://www.mathworks.com/help/
• A Better Way To Learn. (n.d.). Retrieved from https://www.osmosis.org/prime-ecg-series?utm_source=youtube&utm_medium=video_description&utm_campaign=ecg_basics&utm_content=ecg_basics